## Slide 1: Mapping Defect location & Case Study

## Slide 2: HBM Test methods
Chip_detection: Special circuitry surrounding DRAM edges to detect die crack or chipping.
  Log output: showed SID # only
MBIST_March: Read Modified Write (RMW)
  Test methodology: Read one and write zero to cells one by one
  Log output: HBM#, SID#, Channel#, Psudo channel#, Bank#, 16 memory Row addresses to repair
MBIST_scan: Memory bit reflash time test
  Test methodology: Read memory cells with time interval (ex. 32ms) without leakage compensation.
  Log output: HBM#, SID#, Channel#, Psudo channel#, Bank#, 16 memory Row addresses to repair
CDC Circuitry

## Slide 3: HBM Test sequence & test log information
March and Scan test running by Channel and Bank order
One channel has 32banks and one bank has 1024 row addresses
Max. 16 addresses are repairable per channel.
Only 16 addresses are logged per channel as well.

## Slide 4: HBM defect prediction with test logs
Basic factor to determine die edge crack existence.
Not every die edge crack showed CDC failure.
Memory cell defect or control circuit defect
The banks tested after the failing bank are possibly failed as well.
The bank is partially or fully dead & functional.
Clues for prediction
Is there CDC failed?
Failed at March or Scan test? or failed both?
Which bank showed 16 failing addresses?
Failing address count is 16 or less?
What are the failing addresses?
Edge located banks have higher risk of crack
Where is the failed bank located?

## Slide 5: HBM Failure Case Study _ Silicon inner circuitry damage
HBM | Core | Channel | Bank | Failed_Test | failed_address | failed_address_count | Fail_mode
G | 3 | I0 | A0 | March & Scan | [0x14, 0x12, 0x18, 0x8, 0x1c, 0x0, 0xa, 0x1e, 0xe, 0x16, 0x6, 0x1a, 0xc, 0x4, 0x10, 0x2] | 16 | Gross
G | 3 | J0 | A0 | March & Scan | [0x14, 0x12, 0x18, 0x8, 0x1c, 0x0, 0xa, 0x1e, 0xe, 0x16, 0x6, 0x1a, 0xc, 0x4, 0x10, 0x2] | 16 | Gross
G | 3 | K0 | A0 | March & Scan | [0x14, 0x12, 0x18, 0x8, 0x1c, 0x0, 0xa, 0x1e, 0xe, 0x16, 0x6, 0x1a, 0xc, 0x4, 0x10, 0x2] | 16 | Gross
G | 3 | L0 | A0 | March & Scan | [0x14, 0x12, 0x18, 0x8, 0x1c, 0x0, 0xa, 0x1e, 0xe, 0x16, 0x6, 0x1a, 0xc, 0x4, 0x10, 0x2] | 16 | Gross
Is there CDC failed? No
  Possibly not crack related
Failed at March or Scan test? or failed both?
  Failed both, the banks are fully dead
Which bank showed 16 failing addresses?
  All fail banks have 16 addresses.
  Rest of 15 banks B,C,..H&P are possibly failed as well
Failing address count is 16 or less?
What are the failing addresses?
  16 addresses failed and they are continuous.
  The banks are fully dead.
Where is the failed bank located?
  All A0 banks of each channel at the die top edge
Review Result
  Entire banks are not working due to Power supply or defective control circuitry.
  The banks or memory cells are not defective. Buffer die or memory controller problem.
CH
I
CH
J
CH
K
CH
L

## Slide 6: HBM Failure Case Study _ Lateral Crack
Is there CDC failed? No
Failed at March or Scan test? or failed both?
  Failed both, the banks are fully or partially dead
Which bank showed 16 failing addresses?
  All fail banks have 16 addresses.
  Rest of 15 banks J,K,L..P are possibly failed as well
Failing address count is 16 or less?
What are the failing addresses?
  16 addresses failed and they are continuous.
  The banks are fully dead.
Where is the failed bank located?
  Bottom Corner, Bank I0 in Ch A & B
Review Result
  Banks located bottom left corner are dead. (Banks A to H are functional.)
  The banks located corner edge are defective. Possibly crack related
: Possible crack location
HBM | Core | Channel | Bank | Failed_Test | failed_address | failed_address_count | Fail_mode
B | 7 | A0 | I0 | March & Scan | [0xa, 0x16, 0x6, 0x0, 0x1c, 0x12, 0x1e, 0xe, 0x2, 0x4, 0x18, 0x1a, 0xc, 0x8, 0x14, 0x10] | 16 | cell
B | 7 | B0 | I0 | March & Scan | [0xa, 0x16, 0x6, 0x0, 0x1c, 0x12, 0x1e, 0xe, 0x2, 0x4, 0x18, 0x1a, 0xc, 0x8, 0x14, 0x10] | 16 | cell
Crack
Crack
CDC
PFA
CH
A
CH
B

## Slide 7: HBM Failure Case Study _ Vertical Crack
Is there CDC failed? No
Failed at March or Scan test? or failed both?
  Failed both, the banks are fully or partially dead
Which bank showed 16 failing addresses?
  All fail banks have 16 addresses.
  Rest of 15 banks C,D,E..P are possibly failed as well
Failing address count is 16 or less?
What are the failing addresses?
  16 addresses failed and they are continuous.
  But the starting address is not 0X0, The banks are partially dead.
Where is the failed bank located?
  Top Corner, Bank B0 in Ch D
Review Result
  Banks located top left corner are partially dead.
    Failed address is not starting from zero
  The banks located corner edge are defective. Possibly crack related
: Possible crack location
Crack
HBM | Core | Channel | Bank | Failed_Test | failed_address | failed_address_count | Fail_mode
D | 2 | H0 | B0 | March & Scan | [0x1414, 0x140a, 0x1412, 0x1416, 0x141a, 0x141c, 0x140e, 0x1418, 0x141e, 0x1410, 0x140c, 0x1406, 0x1408, 0x1404, 0x1400, 0x1402] | 16 | cell
PFA
CH
H

## Slide 8: HBM Failure Case Study _ Silicon Internal Circuitry – Functional
Is there CDC failed? No
Failed at March or Scan test? or failed both?
  Failed both but failing addresses are different
  The memory cells are some how functional.
Which bank showed 16 failing addresses?
  All fail banks have 16 addresses.
  Rest of 15 banks C,D,E..P are possibly failed as well
Failing address count is 16 or less?
What are the failing addresses?
  16 addresses failed and addresses are random
Where is the failed bank located?
  Top Corner, Bank B0 in Ch A
Review Result
  Banks located top left corner are functional failure.
  Memory cell functional failure. Memory address or bit level issue.
HBM | Core | Channel | Bank |  | Address_failed | fail_addr_count
E | 9 | A0 | B0 | March | 0x1852,0x18b2,0x18c1,0x18d9,0x18ff,0x190a,0x1912,0x1914,0x1942,0x1952,0x1959,0x195f,0x1966,0x196c,0x1971,0x197c | 16
E | 9 | A0 | B0 | Scan | 0xb26,0x1857,0x1912,0x1942,0x19f9,0x1a29,0x1a66,0x1a85,0x1aa9,0x1aba,0x1ae0,0x1ae5,0x1aea,0x1b10,0x1b26,0x1b32 | 16
No obvious die edge discoloration/ crack was observed along right edge.

## Slide 9: Actions taken to prevent gross damage

## Slide 10: Failure mechanism – BEOL internal crack
Crack occur due to the adhesion of the dicing tape.
Chill & Expansion: Decrease adhesion of the dicing tape.
Ejector control parameter optimization: Speed and tilt

## Slide 11: Failure mechanism – Lateral Crack
OCD: Optical Critical Dimension
OS: Oxide Site
Lateral crack starts left and right-side edges
Because
special patterns are located along these saw lines

## Slide 12: HBM Failure Library & Automated Defect Mapping Tool
Log review result & Defect Location mapping
HBM Library
Defect Mapping
Log Review
Log summary
Lib Filters
Tables

## Slide 13: HBM test log review history with Automated Defect Mapping tool
HBM Temp Cycle DOE;
  120 HBM failure are reviewed, and 3 cases were performed PFA.
  3/3 Physical defects were found at the suspected location from the log review.
Production – NPI failure;
  7 HBM failure cases were requested for log review
  2 cases were performed PFA and found defect at one case.
SMR0167714 – FT failure;
  3 HBM failures were requested for log review
  2 of them were selected and being performed PFA @ SEC